STMP1(A13)-EVB
User Manual
Rev.1.0	May 2021
olimex.com

# Overview

STMP1(A13)-EVB is evaluation board for STMP15x-SOM or A13-SOM System On Module running Linux mainline Kernel and Uboot on ST Microelectronics industrial grade Dual Core Cortex-A7 ARM SOC.
As A13-SOM and STMP15x-SOM share same pinout this evaluation board is suitable also for A13-SOM System On Module.
Top view:

## General information

STM32MP15X SOC are Dual-core Arm Cortex-A7 running up to 800 MHz and Cortex-M4 at 209 MHz combined with a LCD interface, dedicated 3D graphics processing unit (GPU).

STMP1(A13)-EVB demo evaluation board is produced only in commercial temperature grade 0-70C.
## Order codes

STMP1(A13)-EVB	only evaluation board for STMP15x-SOM or A13-SOM, does not include SOM module which have to be bough separately

## STMP1(A13)-EVB Features

- 0.05 inch (1.27 mm) connectors for STMP15x-SOM or A13-SOM
- Two High Speed USB 2.0 Hosts
- High Speed USB 2.0 OTG
- 10/100Mb Ethernet connector
- WiFi / Bluetooth module with PCB antenna and option for external antenna
- Flash module connector for: SPI, eMMC, NAND Flash options
- 3.5mm Audio jack for microphone
- 3.5mm Audio jack for headphones
- UEXT connector
- GPIO connector
- 40 pin 0.05 inch (1.27 mm) step connector compatible with LCD-OLinuXino
- Power supply connector 5VDC

# Power supply

STMP1(A13)-EVB requires +5V, 0.2A to operate.
Do not apply more than 5V as this would damage the board.
Power consumption (including SOM module) is:
- around 0.4 A during boot
- around 0.6A when working at full speed
- around 1.2A when working at full speed and charge the LiPo battery

# Connectors
## LCD

RGB LCD signals and I2C connector to digital touch panel interface.

## GPIO

Right angle 20 pin connector with 2x I2C, UART, SDMMC, 2 GPIO, NRST, +3.3V and GND.

## UEXT

UEXT connector for attaching different modules and sensors to SPI, UART, I2C:

# Revision History
Revision 1.0 May 2021

# Contact information

Headquarters and Factory address:

OLIMEX Ltd
ul. Pravda 2
Plovdiv 4000
BULGARIA

Sales:	sales@olimex.com
Technical Support:	support@olimex.com
Corporate Website:	www.olimex.com

For latest news and developments - follow our
- Blog
- GitHub
- Twitter
- Facebook
- Mastodon
- Pluspora
- IRC
- flicr